## Slide 1
BRAHMANAND KARANJEKAR INSTITUTE
OF TECHNOLOGY , SAKOLI
MICROPROJECT
Collect minimum five types of Rocks Specimen in your area and compare their properties with respect to Geotechnical Engineering aspect
PRESENTED BY :
Sahil Praphullakumar Walde
Uday Prakash Marbate
Sumit Doneshwar Kadao
Aman Bandu Barsagade
UNDER THE GUIDANCE OF
P. W. Bhenderkar
Sub :- GTE

## Slide 2
INDEX
introduction of Granite
Properties of granite with Respect to Geotechnical Engineering Aspect
introduction of Besalt
Properties of Besalt with Respect to Geotechnical Engineering Aspect
Introduction of Sandstone
Properties of Sandstone with Respect to Geotechnical Engineering Aspect
Introduction of Limestone
Properties of Limestone with Respect to Geotechnical Engineering Aspect
Inroduction of Marble
Properties of Marble with Respect to Geotechnical Engineering Aspect
Conclusion

## Slide 3
Granite is an intrusive igneous rock, meaning it forms from magma that cools and solidifies deep within the Earth's crust.
The slow cooling process allows for the formation of large crystals, giving granite its characteristic coarse-grained texture.
Granite is found in large formations such as batholiths, and is a very common rock type within continental crust.
Granite :
This is a common intrusive igneous rock.
It's characterized by its coarse-grained texture, with visible crystals of quartz, feldspar, and mica.
It's often used in construction due to its durability.
Characterstics :

## Slide 4
Properties with Respect to Geotechnical Engineering Aspect :-
Strength:
  Generally has high compressive strength, making it suitable for foundations, retaining walls, and as a strong aggregate in concrete and asphalt.
Durability:
Very durable and resistant to weathering and abrasion due to its interlocking crystalline structure and hard mineral composition (quartz and feldspar).
Permeability:
  Typically has low permeability due to the tight interlocking of crystals. However, fractures and joints within a granite mass can significantly increase permeability.
Fracture Characteristics:
  Tends to fracture along existing joints and weaknesses. The nature of these discontinuities is critical for rock mass stability analysis.

## Slide 5
Fine-grained (aphanitic) - individual mineral crystals are too small to see without magnification.
Predominantly composed of dark-colored ferromagnesian minerals like pyroxene and olivine, and plagioclase feldspar.
Typically dark-colored, Relatively dense. Moderately hard.
Basalt :
Extrusive igneous rock, meaning it cooled quickly at the Earth's surface from lava.
Fine-grained, dark-colored (black or dark gray). May have small holes (vesicles) if gases were trapped during cooling.
Common in lava flows and volcanic regions, including oceanic crust.
Characterstics :

## Slide 6
Properties with Respect to Geotechnical Engineering Aspect :-
Strength:
  Generally has high compressive strength, similar to or sometimes even higher than granite. Suitable for similar applications as granite.
Durability:
  Can be very durable, especially the denser varieties. However, some basalts can be susceptible to weathering depending on their mineral composition and porosity (e.g., vesicular basalts might be more prone to freeze-thaw damage).
Permeability:
  Typically has low permeability in its dense form. However, vesicular basalts can have significant permeability due to the presence of voids. Fractures and cooling joints in basalt flows also contribute to permeability.
Fracture Characteristics:
  Often exhibits columnar jointing due to cooling, which can influence the stability of rock masses.

## Slide 7
composed of cemented sand-sized grains that you can often see and feel. The grains can be rounded or angular.
Primarily composed of quartz grains, but can also contain feldspar, mica, and rock fragments.
Varies widely depending on the mineral composition and cement, including tan, brown, red, gray, and white.
Sandstone :
Clastic sedimentary rock formed from the cementation of sand-sized grains.
Gritty texture due to the sand grains. Color varies widely (tan, brown, red, gray, white) depending on the minerals and cement present. May show layering.
Common in many environments, from deserts to beaches to riverbeds. Used as building stone.
Characterstics :

## Slide 8
Properties with Respect to Geotechnical Engineering Aspect :-
Strength:
  Compressive strength varies widely depending on the degree of cementation, mineral composition, and porosity. Weakly cemented sandstones can be very weak, while well-cemented quartz sandstones can be quite strong.
Durability:
  Durability also varies greatly. Poorly cemented sandstones are susceptible to weathering (disintegration, abrasion) and erosion. The type of cement influences durability (e.g., silica cement is generally more durable than clay cement).
Permeability:
  Generally has higher permeability compared to dense igneous and metamorphic rocks due to the interconnected pore spaces between the sand grains. This makes it an important aquifer rock. Permeability depends on grain size, sorting, and the amount of cement.
Density/Specific Gravity:
  Density and specific gravity vary depending on porosity and mineral composition. Generally lower than dense igneous rocks.

## Slide 9
Can be variable. Bioclastic limestone may show visible shells and fragments. Chemical limestone can be fine-grained and dense.
Primarily composed of calcium carbonate (calcite - CaCO₃). May contain impurities like clay, silt, and sand.
Typically light-colored, including white, gray, and tan. Can be darker if it contains organic matter.
Limestone :
Can be either biogenic (formed from the accumulation of shells and skeletal remains of marine organisms) or chemical (precipitated from water).
Typically light-colored (white, gray, tan). Can contain visible fossils. Reacts (fizzes) with dilute hydrochloric acid.
Found in areas that were once covered by shallow seas. Used in construction and for making cement.
Characterstics :

## Slide 10
Properties with Respect to Geotechnical Engineering Aspect :-
Strength:
  Compressive strength varies depending on the density, crystallinity, and presence of impurities. Some limestones can be quite strong, while others are relatively weak.
Durability:
  Can be susceptible to chemical weathering (dissolution by acidic water) due to its calcium carbonate composition. Physical weathering (freeze-thaw) can also be a concern in porous varieties.
Permeability:
  Permeability can vary greatly depending on the presence of fractures, bedding planes, and dissolution features (karst topography). Some limestones can be highly permeable.
Other Geotechnical Concerns:
  Susceptible to the formation of sinkholes and cavities in karst terrains, which can pose significant challenges for construction.

## Slide 11
Non-foliated (lacks a layered or banded appearance). Typically medium to coarse-grained with interlocking crystals that have recrystallized.
Primarily composed of recrystallized calcite (from limestone) or dolomite (from dolostone). May contain various impurities that create different colors and veining.
Wide range of colors, including white, gray, pink, black, green, and various shades in between, often with characteristic veins or swirls.
Marble :
Non-foliated metamorphic rock formed from the metamorphism of limestone or dolostone.
Medium to coarse-grained texture with interlocking crystals. Wide range of colors, often with veins.
Used for sculptures, countertops, and building decoration. Forms in areas that have undergone significant heat and pressure, often at convergent plate boundaries.
Characterstics :

## Slide 12
Properties with Respect to Geotechnical Engineering Aspect :-
Strength:
  Marble generally exhibits high uniaxial compressive strength (UCS), classifying it as a strong rock. This is crucial for its use in structural applications and its behavior as bedrock.
Durability:
  Marble typically has low water absorption, which contributes to its durability and resistance to freeze-thaw damage. However, some types can be more porous..
Permeability:
  Generally, intact marble has low porosity and permeability. However, the presence of fractures, joints, and bedding planes can significantly increase its bulk permeability, affecting groundwater flow and potential for instability.
Physical Properties:
  Marble has a moderate specific gravity, typically ranging from 2.6 to 2.8 g/cm³. This is important for calculating overburden stresses and the weight of marble structures.

## Slide 13
Conclusion :-
Five rock types from Indore showed varied geotechnical properties. Strong, durable rocks (like potential basalt/granite) suit heavy foundations and aggregate. Weaker, less durable rocks (like potential sandstone/shale) pose challenges for stability and require careful consideration. Limestone (if present) suggests potential karst issues. Site-specific investigations are crucial to accurately assess rock mass behavior and ensure safe, economical construction.

## Slide 14
THANK YOU